## Slide 1: Week 1: Discrete Event Systems & Supervisory Control
PhD Preparation — Holonic Demanufacturing
under Structural Uncertainty

## Slide 2: Week 1 — Overview
Day 1: DES foundations — what is a DES, event alphabets
Day 2: Automata for DES — DFA, marked states, languages
Day 3: Supervisory Control Theory — plant/supervisor split
Day 4: Controllability & Observability
Day 5: Safety, Liveness, Blocking/Nonblocking
Day 6: Complete worked example — automaton + supervisor
Day 7: Introduction to Petri Nets

## Slide 3: What is a Discrete-Event System?
State changes at discrete instants, triggered by events
Not time-driven — the system waits for something to happen
Natural fit for manufacturing/demanufacturing cells:
→ arrivals, inspections, faults, routing decisions
Key modelling primitive: the EVENT
Source: Cassandras, Discrete Event Systems (EOLSS)

## Slide 4: Finite Automata for DES
Plant automaton: G = (Q, Σ, δ, q₀, Qₘ)
Q = finite set of states
Σ = event alphabet
δ = transition function (state × event → state)
q₀ = initial state
Qₘ = marked states (task completion)
Generated language L(G): all possible event strings
Marked language Lₘ(G): strings ending in marked states
Source: Raisch, DES & Hybrid Systems, §4.5.1

## Slide 5
The Plant / Supervisor Feedback Loop
Plant G
• Plant G models ALL possible behaviour
• Including unsafe transitions
• Generates events (some controllable, some not)
Supervisor S
• Supervisor S restricts behaviour
• Observes events
• Disables controllable events
• Cannot prevent uncontrollable events

## Slide 6
Controllable vs Uncontrollable Events
Property | Controllable (Σ_c) | Uncontrollable (Σ_uc)
Supervisor can... | Disable / prevent | NOT prevent
Typical source | Actuator commands | Sensor readings, faults
Example | unscrew_cover, route_recycle | arrival, inspect_ok, fault
Engineering rule | Commands you issue | Outcomes you observe

## Slide 7: Observability & Partial Observation
Observable events (Σ_o): supervisor sees them happen
Unobservable events: happen silently
Natural projection P: Σ* → Σ_o* (erases unobservable events)
Challenge: if two strings look the same under P,
the supervisor must make the SAME control decision
Practical impact: hidden damage, unconfirmed actuator commands
Source: Cai & Wonham (2020), pp. 8–9

## Slide 8
Safety vs Liveness
Safety
• "Nothing bad ever happens"
• System never enters forbidden states
• Enforced by disabling unsafe transitions
• Example: never recycle without battery removal
Liveness / Nonblocking
• "Something good eventually happens"
• System can always make progress
• Can always reach a marked (completion) state
• Example: unit can always be processed to done

## Slide 9: Blocking, Nonblocking, Deadlock, Livelock
Nonblocking: every reachable state can reach a marked state
Formally: L̄ₘ(G) = L(G)
Deadlock: no transitions enabled (system is stuck)
Livelock: transitions exist but no path to marked state
Reachable: forward from q₀
Coreachable: backward from Qₘ
Trim = reachable ∩ coreachable
Source: Raisch, p. 75; Cai & Wonham (2020), p. 2

## Slide 10: Worked Example: Demanufacturing Cell — Plant
Scenario: laptop intake → inspection → open/battery → recycle/quarantine
States: Idle, Intake, Inspected_OK, Inspected_Suspect,
Opened, Battery_Removed, Recycle_Done, Quarantine_Done
Σ_c = {unscrew_cover, remove_battery, route_recycle, route_quarantine}
Σ_uc = {arrival, inspect_ok, inspect_sus}
Marked states = {Recycle_Done, Quarantine_Done}

## Slide 11
Worked Example: Supervisor Rule Table
State | Enabled Σ_c | Disabled Σ_c | Rule
Inspected_OK | unscrew_cover, route_quarantine | route_recycle | S2
Inspected_Suspect | route_quarantine | unscrew_cover, route_recycle | S1
Opened | remove_battery, route_quarantine | route_recycle | S2
Battery_Removed | route_recycle, route_quarantine | — | —

## Slide 12: Introduction to Petri Nets
Bipartite graph: places (circles) + transitions (rectangles)
Tokens in places represent state / resource availability
Firing: transition consumes input tokens, produces output tokens
Advantages over automata:
→ Natural resource contention modelling (robot, station)
→ Concurrency without state explosion
→ Place invariants for structural safety
Source: Murata, Petri Nets (1989 tutorial paper)

## Slide 13: Petri Net: Demanufacturing Cell
Flow places: Unit_In → Wait_Inspect → OK/SUS → OPEN → ...
Resource places: INSPECTOR_FREE, ROBOT_FREE
Status places: SAFE_FLAG/HAZARD_FLAG, BATT_IN/BATT_OUT
Key invariants:
INSPECTOR_FREE = 1 (always available)
ROBOT_FREE = 1 (always available)
SAFE_FLAG + HAZARD_FLAG = 1 (boolean)
BATT_IN + BATT_OUT = 1 (boolean)
Supervisor disables: unscrew_hazard, recycle_direct

## Slide 14: Week 1 — Key Takeaways
1. Demanufacturing cells are naturally DES (event-driven)
2. Plant automaton models ALL physically possible behaviour
3. Supervisor disables controllable events to enforce safety
4. Uncontrollable events constrain what any supervisor can achieve
5. Nonblocking guarantees the system can always complete safely
6. Petri nets complement automata for resource/concurrency modelling
7. The supervisor-enabled set is the formal foundation
for all higher layers (twin, learning, mediation)

## Slide 15: Recommended Next Steps — Week 2
Week 2 focus: Structural Uncertainty & Belief States
→ What happens when events are partially observable?
→ Belief states: distributions over possible states
→ Information-state supervisors
→ Connection to the digital twin's state estimation
Tools: same cell model, extended with unobservable events